## Slide 1
Parts of a Computer
KS3 ICT for Grade 8

## Slide 2
Parts of a Computer
Parts of the computer
Identification of the key input devices, their uses, and advantages and disadvantages.
Identification of the key output devices, their uses, and advantages and disadvantages.

## Slide 3
Parts of a Computer
The Computer
Input devices
Output devices

## Slide 4
The computer
Input and output
Inside

## Slide 5
The computer
Motherboard
Inside
Notes: The motherboard serves as a single platform to connect all of the parts of a computer together. A motherboard connects CPU, memory, hard drives, optical drives, video card, sound card, and other ports and expansion cards directly or via cables. It can be considered as the backbone of a computer.
Features of Motherboard
A motherboard comes with following features:
Motherboard varies greatly in supporting various types of components.
Normally a motherboard supports a single type of CPU and few types of memories.
Video Cards, Hard disks, Sound Cards have to be compatible with motherboard to function properly
Motherboards, cases and power supplies must be compatible to work properly together.
Popular Manufacturers
Intel
ASUS
AOpen
ABIT
Biostar
Gigabyte
MSI
Description of Motherboard
The motherboard is mounted inside the case and is securely attached via small screws through pre-drilled holes. Motherboard contains ports to connect all of the internal components. It provides a single socket for CPU whereas for memory, normally one or more slots are available. Motherboards provide ports to attach floppy drive, hard drive, and optical drives via ribbon cables. Motherboard carries fans and a special port designed for power supply.
There is a peripheral card slot in front of the motherboard using which video cards, sound cards and other expansion cards can be connected to motherboard.
On the left side, motherboards carry a number of ports to connect monitor, printer, mouse, keyboard, speaker, and network cables. Motherboards also provide USB ports which allow compatible devices to be connected in plug-in/plug-out fashion for example, pen drive, digital cameras etc.

## Slide 6
The computer
Soundcard
Inside

## Slide 7
The computer
Graphic card
Inside

## Slide 8
The computer
Internal memory
Inside
Work memory, RAM
Notes: 1Bit (Binary Digit)A binary digit is logical 0 and 1 representing a passive or an active state of a component in an electric circuit.2NibbleA group of 4 bits is called nibble.3ByteA group of 8 bits is called byte. A byte is the smallest unit which can represent a data item or a character.4WordA computer word, like a byte, is a group of fixed number of bits processed as a unit which varies from computer to computer but is fixed for each computer.
The length of a computer word is called word-size or word length and it may be as small as 8 bits or may be as long as 96 bits. A computer stores the information in the form of computer words.
Few higher storage units are following
Sr.No.UnitDescription1Kilobyte (KB)1 KB = 1024 Bytes2Megabyte (MB)1 MB = 1024 KB3GigaByte (GB)1 GB = 1024 MB4TeraByte (TB1 TB = 1024 GB5PetaByte (PB)1 PB = 1024 TB
RAM(Random Access Memory) is the internal memory of the CPU for storing data, program and program result. It is read/write memory which stores data until the machine is working. As soon as the machine is switched off, data is erased.
Access time in RAM is independent of the address that is, each storage location inside the memory is as easy to reach as other locations and takes the same amount of time. Data in the RAM can be accessed randomly but it is very expensive.
RAM is volatile, i.e. data stored in it is lost when we switch off the computer or if there is a power failure. Hence a backup uninterruptible power system(UPS) is often used with computers. RAM is small, both in terms of its physical size and in the amount of data it can hold.
RAM is of two types
Static RAM (SRAM)
Dynamic RAM (DRAM)
Static RAM (SRAM)
The word static indicates that the memory retains its contents as long as power is being supplied. However, data is lost when the power gets down due to volatile nature. SRAM chips use a matrix of 6-transistors and no capacitors. Transistors do not require power to prevent leakage, so SRAM need not have to be refreshed on a regular basis.
Because of the extra space in the matrix, SRAM uses more chips than DRAM for the same amount of storage space, thus making the manufacturing costs higher. So SRAM is used as cache memory and has very fast access.
Characteristic of the Static RAM
It has long life
There is no need to refresh
Faster
Used as cache memory
Large size
Expensive
High power consumption
Dynamic RAM (DRAM)
DRAM, unlike SRAM, must be continually refreshed in order to maintain the data. This is done by placing the memory on a refresh circuit that rewrites the data several hundred times per second. DRAM is used for most system memory because it is cheap and small. All DRAMs are made up of memory cells which are composed of one capacitor and one transistor.
Characteristics of the Dynamic RAM
It has short data lifetime
Need to be refreshed continuously
Slower as compared to SRAM
Used as RAM
Lesser in size
Less expensive
Less power consumption
Previous Page
Print
PDF
Next Page
Advertisements

## Slide 9
The computer
Hard drives
Inside
5600
7200
10000

## Slide 10
The computer
Processor CPU
Inside
Notes: CPU consists of the following features:
CPU is considered as the brain of the computer.
CPU performs all types of data processing operations.
It stores data, intermediate results and instructions(program).
It controls the operation of all parts of computer.
Memory or Storage Unit
This unit can store instructions, data and intermediate results. This unit supplies information to the other units of the computer when needed. It is also known as internal storage unit or main memory or primary storage or Random access memory(RAM).
Its size affects speed, power and capability. Primary memory and secondary memory are two types of memories in the computer. Functions of memory unit are:
It stores all the data and the instructions required for processing.
It stores intermediate results of processing.
It stores final results of processing before these results are released to an output device.
All inputs and outputs are transmitted through main memory.
Control Unit
This unit controls the operations of all parts of computer but does not carry out any actual data processing operations.
Functions of this unit are:
It is responsible for controlling the transfer of data and instructions among other units of a computer.
It manages and coordinates all the units of the computer.
It obtains the instructions from the memory, interprets them, and directs the operation of the computer.
It communicates with Input/Output devices for transfer of data or results from storage.
It does not process or store data.
ALU(Arithmetic Logic Unit)
This unit consists of two subsections namely
Arithmetic section
Logic Section
Arithmetic Section
Function of arithmetic section is to perform arithmetic operations like addition, subtraction, multiplication and division. All complex operations are done by making repetitive use of above operations.
Logic Section
Function of logic section is to perform logic operations such as comparing, selecting, matching and merging of data.

## Slide 11
The computer
Computer fans
Inside
Notes: CPU consists of the following features:
CPU is considered as the brain of the computer.
CPU performs all types of data processing operations.
It stores data, intermediate results and instructions(program).
It controls the operation of all parts of computer.
Memory or Storage Unit
This unit can store instructions, data and intermediate results. This unit supplies information to the other units of the computer when needed. It is also known as internal storage unit or main memory or primary storage or Random access memory(RAM).
Its size affects speed, power and capability. Primary memory and secondary memory are two types of memories in the computer. Functions of memory unit are:
It stores all the data and the instructions required for processing.
It stores intermediate results of processing.
It stores final results of processing before these results are released to an output device.
All inputs and outputs are transmitted through main memory.
Control Unit
This unit controls the operations of all parts of computer but does not carry out any actual data processing operations.
Functions of this unit are:
It is responsible for controlling the transfer of data and instructions among other units of a computer.
It manages and coordinates all the units of the computer.
It obtains the instructions from the memory, interprets them, and directs the operation of the computer.
It communicates with Input/Output devices for transfer of data or results from storage.
It does not process or store data.
ALU(Arithmetic Logic Unit)
This unit consists of two subsections namely
Arithmetic section
Logic Section
Arithmetic Section
Function of arithmetic section is to perform arithmetic operations like addition, subtraction, multiplication and division. All complex operations are done by making repetitive use of above operations.
Logic Section
Function of logic section is to perform logic operations such as comparing, selecting, matching and merging of data.

## Slide 12
The computer
Computer fans
Inside
Notes: CPU consists of the following features:
CPU is considered as the brain of the computer.
CPU performs all types of data processing operations.
It stores data, intermediate results and instructions(program).
It controls the operation of all parts of computer.
Memory or Storage Unit
This unit can store instructions, data and intermediate results. This unit supplies information to the other units of the computer when needed. It is also known as internal storage unit or main memory or primary storage or Random access memory(RAM).
Its size affects speed, power and capability. Primary memory and secondary memory are two types of memories in the computer. Functions of memory unit are:
It stores all the data and the instructions required for processing.
It stores intermediate results of processing.
It stores final results of processing before these results are released to an output device.
All inputs and outputs are transmitted through main memory.
Control Unit
This unit controls the operations of all parts of computer but does not carry out any actual data processing operations.
Functions of this unit are:
It is responsible for controlling the transfer of data and instructions among other units of a computer.
It manages and coordinates all the units of the computer.
It obtains the instructions from the memory, interprets them, and directs the operation of the computer.
It communicates with Input/Output devices for transfer of data or results from storage.
It does not process or store data.
ALU(Arithmetic Logic Unit)
This unit consists of two subsections namely
Arithmetic section
Logic Section
Arithmetic Section
Function of arithmetic section is to perform arithmetic operations like addition, subtraction, multiplication and division. All complex operations are done by making repetitive use of above operations.
Logic Section
Function of logic section is to perform logic operations such as comparing, selecting, matching and merging of data.